2021 OSAGE “2148 WARRIOR” TYPE I

2021 RAM “4500 HD”

STANDARD FEATURES

( MEMBER AMD / NTEA & RAM PRO-CARE (

( CERTIFIED KKK-1822-F & ALL REVISIONS (

( CERTIFIED CAAS GVS V2.0 (

## CHASSIS

( 2021 Ram 4500 w/ AH2 Amb Prep Pkg

( 168.5” Wheelbase w/ Dual Rear Wheels

( GVWR:  16,500 LBS

( 6.7 L 16 Cummins Turbo Diesel

( Ram Engine Hour Meter

( Voltage Monitoring Auto Idle Up System

( Allison 6-Speed Automatic Transmission

w/ Tow/Haul Mode

( 4-Wheel Disc Brakes w/ ABS

( Stainless Steel Wheel Inserts

( Aluminum Diamond Plate Running Boards

( Rear Mud Flaps

( Dual Air Bags

( Dodge SLT Trim Package

( Dual Map Lights

( Tilt Steering Wheel & Cruise Control

( Electric Windows & Door Locks

( Keyless Remote Entry

( AM/FM Stereo Clock Radio w/ CD & Cassette

( Clothe High Back Seats

( Rubber Floor Mat I.L.O. Carpet

( OEM Mirrors, Heated and Power Adjust

( Daytime Running Lights

Choice of 2WD or 4WD

## MODULE

( Module Dimensions:

148” L x 83” H x 96” W

( Totally “Seamless” Body Construction

( Exterior Side & Roof Panels .125” Aluminum

( One-Piece Exterior Side Panels

( One-Piece Crowned Roof

( Frame Members 2” x 2” Aluminum Tubing

( Frame Members on 12” Centers

( Diamond Plate Shields:

* Across Lower Rear of Body

* Across Lower Front of Body

* Lower 1/3 of Entry Doors

( All Exterior Doors “Pan-Formed” / Extruded

Double Break Construction

( All Body Openings “Seamless”

( All Door Latches Mounted Behind Gaskets

( Exterior Compartment @ Front Left for

Storage of Oxygen Tank and Back Boards

( Curbside Backboard Storage

( Exterior Compartment Adjustable Shelving

( Exterior Compartment Lighting

( Cast “Grabber” Door Holders

( Lower Body Impact Rub Rails

( Polished Stainless Steel Fenderettes

( Grip Strut Rear Step Bumper w/

4” x 18” Dock Bumpers

( Automotive Undercoating

## WARNING SYSTEM

( Two Red Whelen ION-T LED’s Mounted in

Chrome Flanges in Grill

( Two Red Whelen ION-T LED’S Mounted in

Chrome Flanges in Front Fenders

( Eight Red LED Whelen 9x7 Modular Lights

( One Clear LED Whelen 9x7 Front Center

Modular Light

( One Amber LED Whelen 9x7 Rear Center

Modular Light

( Two LED Whelen 9x7 Scene Lights Per Side

(Two LED Whelen 9x7 Rear Load Lights

( Primary / Secondary Switching

( Carson SA 400 Siren
( Cast Siren Speaker

( Siren / Horn Switch

( Rear DOT Lighting Whelen LED 4x6 w/

Chrome Flanges: Red Tail / Brake,

Amber Arrow Turn, Reverse

( LED Clearance / Marker Lights

## PAINT & MARKINGS

( 8” Belt Line Paint Stripe				        ( “No Smoking” & “Fasten Seat Belt” Signs

( Base Coat / Clear Coat Modular Paint		        ( Ambulance / Star-of-Life Decals

2021 OSAGE “2148 WARRIOR” TYPE I – 2021 RAM “4500 HD” Gas – Standard Features

ELECTRICAL

( RAM OEM Alternator, 220 Amps

( Digital Voltmeter

( Audible Low Voltage Alarm

( Bosch, Vanner, Cole-Herse &

R/C Tronics Components

( Printed Circuit Board w/ Load Management &

Sequencing System

( LED Diagnostic System

( Wiring Color-Coded and Heat Embossed

Every 6” w/ Function

( Power Distribution Panel Easily Accessible

Via Hinged Access Door in Action Area

( Front Switch Console Mounted on the Floor

( Hinge Mounted Attendant Switch Console

( Control Console Backlighting Dimmer

( Battery Switch Activated via Ignition Switch

( Open Door Warning Light

( Three Light Silent Intercom

( Handheld LED Spotlight, Hardwired

( Whelen Dual Intensity LED Patient

Compartment Dome Lights

( Exterior Weatherproof Shoreline Receptacle

( Two Interior 110V Duplex Receptacles

( Two Interior 12V Cigar Style Receptacles

( One Pre-Wire Antenna Cable

( Electrical Back-up Alarm w/ Auto Re-set

## INTERIOR

( 72” Interior Headroom

( 49” Aisle Width

( All Vertical Corners 1” Radii

( Stainless Steel Aisle Panel, Left Side,

Full Length x 18” x .060”

(  Lon-Plate nonskid Vinyl Flooring

Rolled 3” Up Both Sides of Aisle

( EMT Seat, Rear Facing Pedestal Mounted

Deluxe Seamless Vinyl Captains Chair

( CPR Seat, three piece molded, contoured

cushions

( Squad Bench

( Retractable Seat Belts for All Locations

( Handicap Style, 1 ½” Diameter, Full Length,

Stainless Steel Overhead Grab Rail.  This Rail shall be treated with Agion

Anti-Bacterial Coating.

( Handicap Style, 1 ½” Diameter, Stainless Steel

Door Pulls on Patient Compartment Doors.  These Bars shall be treated with Agion

Anti-Bacterial Coating.

- Double entry step on curbside entry door.

( Sliding “Pass-thru” Window Between Cab

and Patient Compartment

( Padded Bulk-Head Cabinet Doors

( ALS Compartment w/ In/Out Access

( 2 Adjustable & 1 Fixed Shelf in ALS

( R-29 Reflectix Insulation throughout Module

( Thermostatically Controlled Patient

Compartment Heat & Cool System

( 3-Speed Manual Fan Control

( Rear Heat & Cool Unit Mounted Floor Level;

* Moisture Drains Directly Through Floor

* Short Coolant Circulation Distance

* Eliminates Vertical Circulation of Coolant

* Unit Easily Accessible for Maintenance

( Overhead Air Distribution w/ Floor Level   Filtered Air Return for Optimum Circulation

( Two Recessed, Swing-up Dual IV Hangers

( “Zico” Retaining Bracket for Oxygen “M” Cyl

( Three “Ohio” Oxygen Outlets

- Impact #324 Self-Contained Suction System

- Locking Sharps Container (Shipped Loose)

( Locking Drug Compartment

( Clock w/ Sweep Second Hand

( Stryker “Performance Load” Cot Fastener

- Seamless Seat Cushions

## WARRANTY

( Three Year / 36,000 Mile Product Conversion ( Five Year / 100,000 Mile Modular Paint

( Six Year / 72,000 Mile Electrical System ( Lifetime Modular Body Structure

“NON-PRO-RATED”

NOTE: See Warranty Certificate for Details

OSAGE AMBULANCE  ( P.O. BOX 718 ( LINN, MO. 65051

800-822-3634  ( FAX: 573-897-3113

www.osageambulances.com